Cryptography with OpenSSL – Applications
# Lab Report 3
Information Systems Security course (01TYM, 02KRQ)
Politecnico di Torino – AA 2023/24
prepared by:
Anuar Elio Magliari (s317033@studenti.polito.it)
George Florin Eftime (s303483@studenti.polito.it)
# Cryptography applications: integrity
## Message Authentication Codes
### Manual generation of a keyed-digest
- Write down the command dgst of OpenSSL that Alice could to calculate a keyed-digest on the file msg, by using sha256 as base function?
  - openssl dgst -sha256 -hmac key -out msg_digest -hex msg
- What information needs to know Bob to verify this manually constructed keyed-digest?
  - The original plaintext
  - The symmetric key
  - The base function used for the hashing
- Which steps must be performed by Bob to verify the keyed-digest?
  - Once Bob receives the message from Alice, he should calculate the keyed digest by providing the hash function with the symmetric key and the received message. Afterward, using the resulting hash value, he can compare it with the digest provided by Alice and attached to the received message.
- Why this way of constructing a keyed-digest is not secure?
  - An attacker, even if he doesn’t know the key, could append message blocks to the end of the message (or at the beginning, depending on where the key is located) and recalculate the keyed digest.
### Computing an HMAC with OpenSSL
- Write the OpenSSL command used to verify the keyed-digest generated above (hint: to compare two files you can use the command cmp)
  - openssl dgst -sha256 -binary -hmac key -out msg.hmac msg
  - openssl dgst -sha256 -binary -hmac key -out msg.hmac_bob msg
  - cmp msg.hmac msg.hmac_bob (any output if the are equal)
- Is the HMAC that you have just recalculated different from the one you have calculated previously on the original message?
  - openssl dgst -sha256 -binary -hmac key -out msg.hmac_recalculated msg
  - cmp msg.hmac msg.hmac_recalculated
    - Output: msg.hmac msg.hmac_recalculated difference: byte 1, row 1