IPsec and Transport Layer Security
# Lab Report 4
Information Systems Security course (01TYM, 02KRQ)
prepared by:
Anuar Elio Magliari (s317033@studenti.polito.it)
George Florin Eftime (s303483@studenti.polito.it)
Alekos Interrante Bonadia (s319849@studenti.polito.it)

# IPSec and security at IP level
## 3.1 Setting IPsec policies and Security Associations
Which commands do you need to run to flush the SAD and SPD? Which commands do you need to run to check the content of the SAD and SPD databases?
  - In order to flush the SAD the command needed is:
    - ip xfrm state flush
  - For the SPD database the command needed is:
    - ip xfrm policy flush
- which type of traffic is protected with IPsec?
  - In IPsec we protect the payload not the header (AH encapsulates also the real header). We do it with ESP or AH strategy ESP is ok for confidentiality, authentication, integrity and also for protection against replay attacks. Using AH we does not give encryption so usually ESP is preferred. In this solution we are using only ESP algorithm.
- which IPsec protocol is used?
  - The IPsec protocol used are AH and ESP protocols
- which security services are provided?
  - AH: authentication, integrity and protection against replay attacks
  - ESP: almost same functions provided by AH, plus confidentiality
- Which are the cryptographic algorithms used?
  - AES-128-CBC is used in this case
- what are respectively the roles of the Security Association Database (SAD) and of the Security Policy Database (SPD) in the IPsec architecture?
  - SAD (Security association database) is required to offer a valid policy between two IP addresses so between two devices with specific IP. The association is saved in the “DB” and could be then checked using an index (SPI). In this case we are using the indexes 0x1000 for Alice DB and 0x2000 for Bob DB.
- which directives are processed every time Alice sends a new IP packet?
  - The directives that are processed every time Alice sends a new IP packet are: verification of valid index in the SAD and the policies, encryption then encapsulation of payload IP packet then finally sending to the destination
- why are two SAs necessary?
  - The SAs associations are two because even if the association is unidirectional, for a secure bidirectional channel we need to have SA policies in both nodes so that the channel can be secure and both DB (for Alice IP and Bob IP device) should be filled with the other index, key, IP and algorithm. Then, there are two tables, one for outgoing packets and one for incoming packets in each of the two nodes connected.
- which is the purpose of the field SPI present in the IP packets exchanged?
  - SPI is a specific index for each connection channel so there is always a single and unique index of 32 bits associated with a IP in the SAD. The SPI can be manual or random value but always it should be unique
- Which is the scope of the field Seq Number?
  - The purpose of the sequence number within packets is to prevent replay and filtering attacks. In other words, it is a method to protect packets from manipulation by an attacker. It is also used for the integrity check of a packet by the endpoints.

## 3.2 Setting IPsec policies and Security Associations
- ESP with AES-128-CBC and HMAC-SHA1;
  - ip xfrm state add src 192.168.1.43 dst 192.168.1.42 proto esp spi 0x1000 enc aes 0xaa223344556677889900aabbccddeeff auth sha1 0xbbccddeeff00112233445566778899aabbccddeeff
  - ip xfrm state add src 192.168.1.42 dst 192.168.1.43 proto esp spi 0x2000 enc aes 0xbb223344556677889900aabbccddeeff auth sha1 0xaaccddeeff00112233445566778899aabbccddeeff
  - ip xfrm policy add src 192.168.1.43 dst 192.168.1.42 dir out tmpl proto esp mode transport level required
  - ip xfrm policy add src 192.168.1.42 dst 192.168.1.43 dir in tmpl proto esp mode transport level required
- AH with HMAC-SHA1:
  - ip xfrm state add src 192.168.1.43 dst 192.168.1.42 proto ah spi 0x3000 auth sha1 0xbbccddeeff00112233445566778899aabbccddeeff
  - ip xfrm state add src 192.168.1.42 dst 192.168.1.43 proto ah spi 0x4000 auth sha1 0xaaccddeeff00112233445566778899aabbccddeeff
  - ip xfrm policy add src 192.168.1.43 dst 192.168.1.42 dir out tmpl proto ah mode transport level required
  - ip xfrm policy add src 192.168.1.42 dst 192.168.1.43 dir in tmpl proto ah mode transport level required
- ESP with AES-128-CBC and AH with HMAC-SHA1:
  - ip xfrm state add src 192.168.1.43 dst 192.168.1.42 proto esp spi 0x1000 enc aes 0xaa223344556677889900aabbccddeeff
  - ip xfrm state add src 192.168.1.42 dst 192.168.1.43 proto esp spi 0x2000 enc aes 0xbb223344556677889900aabbccddeeff
  - ip xfrm state add src 192.168.1.43 dst 192.168.1.42 proto ah spi 0x3000 auth sha1 0xbbccddeeff00112233445566778899aabbccddeeff
  - ip xfrm state add src 192.168.1.42 dst 192.168.1.43 proto ah spi 0x4000 auth sha1 0xaaccddeeff00112233445566778899aabbccddeeff
  - ip xfrm policy add src 192.168.1.43 dst 192.168.1.42 dir out tmpl proto esp mode transport level required
  - ip xfrm policy add src 192.168.1.42 dst 192.168.1.43 dir in tmpl proto ah mode transport level required
- ESP with AES-128-GCM (RFC-4106) Authenticated Encryption with Associated Data (AEAD).
  - ip xfrm state add src 192.168.1.43 dst 192.168.1.42 proto esp spi 0x1000 aead rfc4106(gcm(aes)) 0xaa223344556677889900aabbccddeeff12345678 96
  - ip xfrm state add src 192.168.1.42 dst 192.168.1.43 proto esp spi 0x2000 aead rfc4106(gcm(aes)) 0xbb223344556677889900aabbccddeeff12345678 96
  - ip xfrm policy add src 192.168.1.43 dst 192.168.1.42 dir out tmpl proto esp mode transport level required
  - ip xfrm policy add src 192.168.1.42 dst 192.168.1.43 dir in tmpl proto esp mode transport level required
- How many SAs and SPs do you need to define to implement the security mechanism 3 (above)?
  - 4 Sas and 2 Sps
- Which is the difference among the configurations 1 and 3 in terms of the structure of the IP packets obtained?

  - ip xfrm policy update src 172.22.16.169 dst 172.22.16.190 dir in tmpl proto esp mode transport

  - ip xfrm policy update src 172.22.16.190 dst 172.22.16.169 dir out tmpl proto ah mode transport

- when is the configuration 2 useful?
  - It is useful when the purpose is to authenticate the packets and the intermediate nodes. Furthermore, it’s faster because it does not need to encrypt.
- what advantage do we have using the configuration 4?
  - With configuration 4 we have a single algorithm for encryption and integrity so low overhead, more efficiency and simpler to implement.
- Choose one of the previous configurations and modify the SPs so that to protect only the TCP protocol messages (and not the messages corresponding to the other protocols). Verify subsequently that the ping packets are not protected, while the TCP traffic remains protected (for example the HTTP traffic).
  - ip xfrm policy add proto tcp dir out priority 1
  - ip xfrm policy add proto tcp dir in priority 1
- Finally, indicate which information is contained in the SAD and in the SPD.

## Performance measurement

	10 KB	100 KB	1MB	10 MB	100 MB
No IPsec/TLS
time [s]	0,12	0,15	0,51	4,03	37,18
speed [kB/s]	84,7	655	1929	2426	1911
ESP transport AES-128-CBC
time [s]	0,35	0,82	0,37	5,21	38,70
speed [kB/s]	28,2	1190	2682	1846	3680
ESP transport AES-128-CBC HMAC-SHA1
time [s]	0,58	0,19	0,45	3,1	28,32
speed [kB/s]	17,2	516	2194	3163	3699
AH transport HMAC-SHA1
time [s]	0,07	0,08	0,37	2,58	27,46
speed [kB/s]	130	1268	2646	3789	2941
ESP AES-128-CBC + AH HMAC-SHA1
time [s]	0,38	0,09	0,42	3,57	27,67
speed [kB/s]	26,45	1122	2336	2737	2614

## The IKE protocol
- How many SAs have been negotiated?
  - There have been a total of 2 SAs negotiations.
- Which kind of security header and which mode is used in the SA? ESP or AH?
  - ESP
- Which algorithms are used?
  - AES_CBC_128
  - HMAC_SHA2_256_128
- Which is the key length used for each algorithm?
  - 128 bits
- In which phase of the IKE protocol is used the configured PSK?
  - The PSK is used during Phase 1 of the IKE protocol. During Phase 1, the PSK is used to authenticate the parties involved and to establish a secure initial communication channel. The PSK is a shared secret that is known to both the initiator and the responder of the IKE negotiation. This shared secret is used to prove the authenticity of each party and to derive the initial keying material for securing the subsequent communication.
# The TLS protocol
- Which cipher suite has been negotiated?
  - Client
  - server

During the handshake, the client presents to the server 91 available cipher suites where the server must choose one of them. In this case, the server choosed TLS_AES_256_GCM_SHA384
- Which TLS version has been negotiated?
  - The version negotiated is the 1.3 version

- Which TLS version has been negotiated?
  - The version negotiated is the 1.2 version

- Which cipher suite has been negotiated?
  - TLS_ECDHE_RSA_WITH_AES_256_GCM_SHA384
- Which algorithm has been used for key exchange?
  - EC Diffie-Hellman

## Configuration of a TLS server
- Which is the purpose of the parameter -no_dhe used so far?
  - By default is set dhe (Diffie Hellman Ephemeral) that is used for the key exchange, instead using the command -no_dhe will disable this option
- What are and in which case can be used the ephemeral mechanisms for key exchange in TLS?
  - Ephemeral Diffie-Hellman (DHE)
    - DHE is used when the forward secrecy is desired
  - Ephemeral Elliptic Curve Diffie-Hellman (ECDHE)
    - ECDHE is used when the computational resource are limited so that it provides strong security with shorter keys
  - RSA Key Exchange with Forward Secrecy (RSA-FS)
    - DHE is generally preferred over RSA because it provides forward secrecy as well. While RSA can be used as an alternative, its reliance on long-term keys poses a security concern.
### Use of Session ID
- For what purpose it is used the “Session ID” in TLS?
  - The session ID is very useful for skipping the phase of algorithm negotiation, enabling the use of the same algorithm decided in the previous session. However, new keys will be generated for the connection
### Client authentication in TLS
- Now try to configure an SSL/TLS server with client authentication. What do you need in the first place?
  - We need to use the certificate for the server (it’s mandatory in the handshake)
- Identify the steps that have changed in the handshake phase of the SSL/TLS protocol.
  - The client has sent its certificate, so during the handshake phase, the server must also verify the client's certificate by checking the entire certificate chain. Thus, we achieve mutual authentication, enhancing security because the peers can engage in confidential communication